## Slide 1: Harnessing the power of fecal microbial communities to assess health risks in the environment
Eric Dubinsky
Lawrence Berkeley National Laboratory

## Slide 2: Microbes love your guts
100 trillion microbial cells in human gut
Diverse: 300 – 1000 species in each gut
At least 80% of species uncultivated, known only by DNA sequencing
Conventional tests do not measure most fecal bacteria

## Slide 3: Community DNA sequence analysis: taking stock of everybody
Comprehensive census of microbial community is cheaper, faster than ever
Opportunity to use communities instead of single markers to identify pathogen sources and health risks
Can develop tests that are far more specific and accurate than current assays for monitoring fecal pollution

## Slide 4: Clean Beaches Project
Use PhyloChip to improve fecal source tracking in recreational waters
Develop new fecal indicator tests based on microbial community differences among suspected fecal sources
Identify bacteria associated with bad water quality at popular California beaches to determine source of contamination

## Slide 6: Fecal samples can be classified based on microbial community composition
Detected 1548 different bacterial subfamilies in fecal samples
Human sources form distinct cluster despite type of waste processing
Little variation among populations of ruminant animals
Variation among populations of each bird species greater than mammals
cow
cow
cow
cow
elk
elk
elk
elk
horse
horse
horse
horse
sea lion
sea lion
sea lion
seal
sewage
sewage
sewage
sewage
sewage
sewage
septage
septage
gull
gull
pelican
gull
gull
pelican
pelican
gull
gull
gull
gull
gull
pigeon
pigeon
cormorant
goose
goose
goose
goose
grazers
pinnipeds
humans
birds
mammals
Notes: Strong potential for source identification based on bacterial community differences

## Slide 7: Field application: sewage spill monitoring
764,000 gallon sewage spill from Sausalito treatment plant into San Francisco Bay (2009)
Were high bacteria counts in Bay due to sewage spill?

## Slide 9: Are human, cattle or wildlife causing water quality problems at popular California beaches?

## Slide 10: Blinded study: PhyloChip the only method that identified all fecal sources
 | True positive rate | Number false positives
Chicken | 100 | 0
Cow | 75 | 1
Deer | 100 | 0
Dog | 100 | 0
Goose | 100 | 2
Gull | 83 | 0
Horse | 100 | 0
Human stool | 100 | 0
Pig | 100 | 0
Pigeon | 100 | 0
Septage | 100 | 0
Sewage | 93 | 0